## Slide 1: 2D Convolution Accelerator
A single channel 2D Convolution accelerator for the PYNQ-Z2.
Dhruv Deshmukh (dad10090)
Luka Kitamura (lk3283)
Faiza Zahin Tasfia (ft2335)

## Slide 2: Overview
Introduction to 2D convolution
Architecture
Verification. A
BD Implementation
Verification. B
Benchmarking
Device Demo
Future Improvements

## Slide 3: 2D Convolution
• Kernel slides across the input image and computes a dot product for each 3×3 region
• The same 9 kernel weights are reused across the entire image
• Valid convolution (no padding) reduces output to (M−2) × (N−2)

## Slide 4: Design Architecture
In/Out FIFO
  Manage for output Backpressure through line buffer
cf mem
  Stores config information
Line Buffer
  Perpetually loading rows of matrix
Mac & Truncate
  Performs the computation and clipping
Bit packer
  8-to-32-bit packer

## Slide 5: CF(Config) Memory
  First 4 transfers go to CF memory
  Elements in row from 0 – 64 to include 0 – 60 supported size
  Number of rows from 0 – 1024 to include 0 – 1023 rows support
  All K’s are 8-bit signed integers so each are 9 bits.
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Reserved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Number of Rows |  |  |  |  |  |  |  |  |  | elements in a row |  |  |  |  | 
Reserved |  |  |  |  | K02 |  |  |  |  |  |  |  |  | k01 |  |  |  |  |  |  |  |  | K00 |  |  |  |  |  |  |  | 
Reserved |  |  |  |  | K12 |  |  |  |  |  |  |  |  | k11 |  |  |  |  |  |  |  |  | K10 |  |  |  |  |  |  |  | 
Reserved |  |  |  |  | K22 |  |  |  |  |  |  |  |  | k21 |  |  |  |  |  |  |  |  | K20 |  |  |  |  |  |  |  | 

## Slide 6: Line Buffer
Receives 32 bit every cycle
Stores it as 8 bit elements
Async access to 3 elements at a time from each row
4 total rows, access 3 at a time

## Slide 7: Line Buffer
Line buffer
Reference Matrix & computation
1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28
29 | 30 | 31 | 32 | 33 | 34 | 35
36 | 37 | 38 | 39 | 40 | 41 | 42
43 | 44 | 45 | 46 | 47 | 48 | 49
1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28

## Slide 8: Line Buffer
Line buffer
Reference Matrix & computation
1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28
29 | 30 | 31 | 32 | 33 | 34 | 35
36 | 37 | 38 | 39 | 40 | 41 | 42
43 | 44 | 45 | 46 | 47 | 48 | 49
29 | 30 | 31 | 32 | 33 | 34 | 35
8 | 9 | 10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28

## Slide 9: Line Buffer
Line buffer
Reference Matrix & computation
1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28
29 | 30 | 31 | 32 | 33 | 34 | 35
36 | 37 | 38 | 39 | 40 | 41 | 42
43 | 44 | 45 | 46 | 47 | 48 | 49
29 | 30 | 31 | 32 | 33 | 34 | 35
36 | 37 | 38 | 39 | 40 | 41 | 42
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28

## Slide 10: Line Buffer
Line buffer
Reference Matrix & computation
1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28
29 | 30 | 31 | 32 | 33 | 34 | 35
36 | 37 | 38 | 39 | 40 | 41 | 42
43 | 44 | 45 | 46 | 47 | 48 | 49
29 | 30 | 31 | 32 | 33 | 34 | 35
36 | 37 | 38 | 39 | 40 | 41 | 42
43 | 44 | 45 | 46 | 47 | 48 | 49
22 | 23 | 24 | 25 | 26 | 27 | 28

## Slide 11: Line Buffer
Line buffer
Reference Matrix & computation
1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28
29 | 30 | 31 | 32 | 33 | 34 | 35
36 | 37 | 38 | 39 | 40 | 41 | 42
43 | 44 | 45 | 46 | 47 | 48 | 49
29 | 30 | 31 | 32 | 33 | 34 | 35
36 | 37 | 38 | 39 | 40 | 41 | 42
43 | 44 | 45 | 46 | 47 | 48 | 49
0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 12: MAC and Truncate
4 stage pipelined
9 multiplications
Additions
0 - 255 Clipping
Answer valid signal
1 pixel per cycle after pipeline fills

## Slide 13: WB Message
(M X N) = (M – 2 X N – 2)
Limitation of %4 elements per row
Scalable number of rows
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Pixel 3 |  |  |  |  |  |  |  | Pixel 2 |  |  |  |  |  |  |  | Pixel 1 |  |  |  |  |  |  |  | Pixel 0 |  |  |  |  |  |  | 

## Slide 14: Transaction example

## Slide 15: Verification. A
Transactions generated in all supported sizes
Simulation depends on 100% Coverage
RTL verified for
  B2B transactions
  Supported images 16x16 to 60x60

## Slide 16: Testbench Outputs

## Slide 17: BD Implementation

## Slide 18: BD Implementation

## Slide 19: Verification. B
Verified implemented design in Hw/Sw
  Test case verified against SciPy convoloution2d
  Sustained test over 1hr for functionality
If interested the log file can be read here

## Slide 20: Benchmarking
Benchmarking done against CPU-only implementation using scipy.signal.convolve2d on an ARM Cortex-A9
Two testcases:
  A: Fixed width of 16 pixels, height varies 16 –> 1000 pixels
  B: Fixed width of 60 pixels, height varies 16 –> 1000 pixels
20,000 random input matrices with random 3x3 kernels for each test
Only timing is measured
  FPGA implementation includes DMA overhead – measures end-to-end accelerator times

## Slide 21: Benchmarking

## Slide 22: Results

## Slide 23: Device Demo
Walk through the projects demo.ipynb to demonstrate the functioning of the device.

## Slide 24: Future Improvements
Multi channel (RGB) Support
  Advantage of 4 possible AXIS channels to DMA
  Better encoding of data, less wasted bits
Multi Core Design
  Reduce lag between buffer fill and computation
Reduce Technical Debt
  Approach design with new knowledge than current implementation
Higher Clock Frequency
  Reduce timing paths, currently (BRAM -> BUFFER -> MAC)